NHMS

2600 Douglas Road, Suite 800, Coral Gables, FL 33134

(305) 854-1711

Property Condition Report

Case Number:

093-601378

Full Address:

7406 Duke Dr

Hudson, FL  34667

Inspection Date:

02-04-2010

Inspection Type:

Property Condition Inspection

Prepared By:

Snow Enterprises, LLC

NOTICE TO ALL PROSPECTIVE PURCHASERS: Pursuant to section 5.3.4 of HUD RFP: R-OPC-22505, you are hereby notified that

the contents of this inspection report are for information only and do not imply any guarantee or warranty of property condition.

Table of Contents

1

Inspection Requirements ............................................................................................................................... 1

1.1

Exclusions of Inspections........................................................................................................................ 1

1.2

Exclusions and Limitations ..................................................................................................................... 1

2

Report Summary............................................................................................................................................ 2

3

Directions to Property.................................................................................................................................... 4

4

Property Information..................................................................................................................................... 4

5

Additional Comments .................................................................................................................................... 4

6

Structure ......................................................................................................................................................... 5

6.1

General Structure Information................................................................................................................. 5

6.2

Structure Checkpoints ............................................................................................................................. 5

6.3

Structure Comments................................................................................................................................ 5

7

Exterior ........................................................................................................................................................... 6

7.1

General Exterior Information .................................................................................................................. 6

7.2

Exterior Checkpoints............................................................................................................................... 6

7.3

Exterior Comments.................................................................................................................................. 6

8

Roof.................................................................................................................................................................. 8

8.1

General Roof Information ....................................................................................................................... 8

8.2

Roof Checkpoints.................................................................................................................................... 8

8.3

Roof Comments....................................................................................................................................... 8

9

Plumbing ......................................................................................................................................................... 9

9.1

General Plumbing Information................................................................................................................ 9

9.2

Plumbing Checkpoints ............................................................................................................................ 9

9.3

Plumbing Comments ............................................................................................................................... 9

10

Electrical ....................................................................................................................................................... 11

10.1

General Electrical Information.............................................................................................................. 11

10.2

Electrical Checkpoints........................................................................................................................... 11

10.3

Electrical Comments ............................................................................................................................. 11

11

HVAC ............................................................................................................................................................ 12

11.1

General HVAC Information.................................................................................................................. 12

11.2

HVAC Checkpoints............................................................................................................................... 12

11.3

HVAC Comments ................................................................................................................................. 13

12

Interior .......................................................................................................................................................... 14

12.1

General Interior Information ................................................................................................................. 14

12.2

Interior Checkpoints.............................................................................................................................. 14

12.3

Interior Comments................................................................................................................................. 14

13

Appliances..................................................................................................................................................... 15

13.1

General Appliances Information ........................................................................................................... 15

Table of Contents (continued)

13.2

Appliances Checkpoints........................................................................................................................ 15

13.3

Appliances Comments........................................................................................................................... 15

14

HOA Information......................................................................................................................................... 16

15

Code Violations............................................................................................................................................. 16

16

Pending Litigation........................................................................................................................................ 16

17

Demo Orders................................................................................................................................................. 16

18

Radon Gas and Mold Notice and Release Agreement .............................................................................. 17

19

Environmental Issues................................................................................................................................... 18

20

Environmental Compliance Record, Attachment 18 in Handbook 4310.5............................................. 19

21

Report Images............................................................................................................................................... 20

Case Number: 093-601378

1

Snow Enterprises, LLC

1

.

INSPECTION REQUIREMENTS

STRUCTURAL COMPONENTS including foundation, floors, walls, columns, ceilings, and roofs.

EXTERIOR OF STRUCTURE including wall claddings, entryway doors, decks, steps, eaves,

driveways, windows, patios, pools/spas, lawns, landscape, retaining walls, sheds/outbuildings, and

fences.

ROOFING including roof coverings, roof drainage systems, flashing, skylights, and chimneys.

PLUMBING including interior water supply and distribution system, interior waste drains and vent

system, hot water system, fuel storage and distribution system, and sump pump.

ELECTRICAL including service entrance conductors, service equipment, main distribution panels,

voltage ratings, a representative number of installed ceiling fans, lighting fixtures, switches and

receptacles, ground fault circuit interrupters, and smoke detectors.

HVAC (Heating Ventilation, Air Conditioning) including permanently installed heating system and its

controls, chimneys, heat distribution system, including fans, pumps, and ducts , and automatic safety

controls.

Normal operating control of the central air conditioning system and the distribution system.

Insulation vapor barriers, ventilation of attic and foundation, kitchen, bathroom and laundry venting

systems, and the operation of any readily accessible attic ventilation fan when temperature permits

INTERIOR including walls, ceilings, floors, steps, cabinets, doors, windows, etc

BUILT-IN KITCHEN APPLIANCES including the observation and operation of dishwasher, range,

trash compactor, garbage disposal, ventilation equipment, permanently installed oven and microwave

oven.

1

.

1

.

Exclusions of Inspection

1

.

2

.

Exclusions and Limitations

This inspection is limited to visual observations of apparent conditions existing at the time of the

inspection only.

This inspection is not intended to provide the purchaser with information regarding

the advisability of this purchase, the market value of the property, the compliance or non-compliance

with codes, ordinances and statutes, the suitability of this property for specialized use, the life

expectancy of any component or system in the property, the presence or absence of pests or insects,

or cosmetic or underground items or items that are not permanently installed. This inspection report

does not address and is not intended to address the possible presence of any danger from any

potentially harmful substance and environmental hazards, including but not limited to radon gas, lead

paint, asbestos, urea formaldehyde (UFFI), toxic or chemical analysis, airborne hazards, polluted

water, or underground oil tanks.

Case Number: 093-601378

2

Snow Enterprises, LLC

2

Report Summary

This summary is provided to highlight those findings that we believe are for information,

significant in nature or which appear to be in immediate need of repair or a safety concern.

This inspection is visual only in areas that were accessible at the time of inspection.  No

dismantling of building components or systems, no destructive testing, no engineering functions,

and no code compliance inspections were performed at the time of the inspection.  The findings

were as follows:

Structure

•

The structure was in satisfactory condition at the time of the inspection.

•

The checkpoints within the "Structure" area of the property condition report pertain to the foundation

areas of the home. This includes slabs, crawlspaces, and basements. Information on Non-structural

issues regarding floors, walls, and ceilings will be found on the "Interior" page of the report.

Exterior

•

At the time of the inspection, the exterior of the structure was in acceptable condition with noted

deficiencies.

Roof

•

At the time of the inspection, there were apparent deficiencies noted regarding the roof of the

structure.

Plumbing

•

The plumbing system was not in working condition at the time of the inspection. The water was

active at the time of the inspection, there were two leaking shut off valves at the exterior of the

structure.

•

There is an irrigation pump at the structure.

•

Wells and septic systems, if present, are inspected only for the presence of obvious visible defects.

The water quality and flow capacity of wells is not determined and the full operational functionality

of septic systems cannot be determined due to the unavailability of water and the extended non-use of

the system.

•

This report reflects general conditions noted during the time of the inspection.  Systems such as

HVAC, Plumbing, and Electrical because of their nature and complexity are subject to deterioration

or breakdown over time that cannot be predicted.

•

Because of this, prospective buyers are strongly urged to obtain a full home inspection prior to

purchase.

Electrical

•

The electrical system was in working condition at the time of the inspection. The system was

powered up using a generator.

•

Electrical systems, if not active, are tested using 220 volt generators.

Case Number: 093-601378

3

Snow Enterprises, LLC

•

This report reflects general conditions noted during the time of the inspection.  Systems such as

HVAC, Plumbing, and Electrical because of their nature and complexity are subject to deterioration

or breakdown over time that cannot be predicted.

•

Because of this, prospective buyers are strongly urged to obtain a full home inspection prior to

purchase.

HVAC

•

The heating system was  in working condition when the structure was connected to a 220V generator.

The AC unit was visually tested due to the low temperature. There is a window AC unit present at the

structure.

•

This report reflects general conditions noted during the time of the inspection.  Systems such as

HVAC, Plumbing, and Electrical because of their nature and complexity are subject to deterioration

or breakdown over time that cannot be predicted.

•

Because of this, prospective buyers are strongly urged to obtain a full home inspection prior to

purchase.

Interior

•

At the time of the inspection, the interior of the structure was in satisfactory condition with noted

deficiencies.

Appliances

•

The appliances that were present were in acceptable condition at the time of the inspection.

Case Number: 093-601378

4

Snow Enterprises, LLC

3

Directions to Property

Automatically Generated via Google Maps -- MAY NOT BE ACCURATE

1. Head east on Lazy Ln toward Diagonal Rd -- 322 ft

2. Lazy Ln turns slightly left and becomes Diagonal Rd -- 0.1 mi

3. Turn left at New York Ave -- 0.3 mi

4. Take the 1st left onto FL-55 S US-19 S -- 2.4 mi

5. Turn left at Country Club Dr -- 0.5 mi

6. Turn right at College Hill Dr -- 361 ft

7. Take the 1st right onto Duke Dr Destination will be on the left -- 240 ft

4

Property Information

Address: 7406 Duke Dr, Hudson, FL 34667

Structure Age: See Appr.

Access to Property: HUD Key

Number of Bathrooms: 2.5

Square Footage: 501-1000 Sq. Ft.

Electric Status: Inactive

Water Status: Active

Gas Status: NA

Occupancy Status: No

5

Additional Comments

Power Company:WRECK

Meter Number:39624673

Water Company:Pas co utilities

41106568

Case Number: 093-601378

5

Snow Enterprises, LLC

6

Structure

This portion of the inspection covers general structural component checkpoints of the subject property

such as foundation, floors, walls, columns, ceilings, basement, etc.

6.1

General Structure Information

Access Method: NA

Foundation Type: Slab

Basement Type: NA

6.2

Structure Checkpoints

Checkpoint

Rating

Comment

Basement Floor:

NA

Beam Supports:

NA

Ceilings:

NA

Cracks:

NV

Crawlspace Door:

NA

Floor:

NA

Footing Drain:

NV

Ground Grade:

S

Insulation:

NV

Joists:

NA

Sill Plate:

NA

Structural:

S

Sub-Flooring:

NA

Walls:

NA

Wood-Ground Distance:

NA

Key:  Y=Yes  N=No  S=Satisfactory  U=Unsatisfactory  MR=Marginal  MG=Missing  NA=Not Applicable  NV=Not Visible

6.3

Structure Comments

The structure was in satisfactory condition at the time of the inspection.

The checkpoints within the "Structure" area of the property condition report pertain to the foundation

areas of the home. This includes slabs, crawlspaces, and basements. Information on Non-structural issues

regarding floors, walls, and ceilings will be found on the "Interior" page of the report.

Case Number: 093-601378

6

Snow Enterprises, LLC

7

Exterior

This portion of the inspection covers general exterior checkpoints of the subject property structure such as

wall claddings, entryway doors, decks, steps, eaves, driveways, windows, patios, pools/spas, lawns,

landscape, retaining walls, sheds/outbuildings, fences, etc.

7.1

General Exterior Information

Exterior Siding: Stucco

Lot Size: Less than one-quarter

Weather Conditions: Clear

Wall Structure: Frame

Temperature: 50-60

7.2

Exterior Checkpoints

Checkpoint

Rating

Comment

Balconies:

NA

Carports:

S

Debris:

S

Decks/Deck Steps:

NA

Driveway:

S

Eaves:

MR

There are damaged eave boards.

Entry Locks:

S

Exterior Door/Locks:

MR

The rear exterior door is damaged but does not prevent it from being

secured.

Fencing/Gates:

MR

There is damaged areas of fencing.

Garage Door:

S

Garage Door Opener:

S

Landscape:

S

Lawn Care:

S

Leaf Removal:

S

Patio:

S

Pool/Spa:

NA

Porches:

NA

Railings:

NA

Retaining Walls:

NA

Sheds and Outbuildings:

MR

The shed door and roof are damaged.

Sidewalks:

S

Siding Condition:

MR

There are damaged shutters.

Snow Removal:

NA

Exterior Steps:

S

Storm/Screen Windows:

MR

There are missing window screens in the structure.

Storm/Screen Doors:

MR

There is missing door hardware.

Windows:

S

Key:  Y=Yes  N=No  S=Satisfactory  U=Unsatisfactory  MR=Marginal  MG=Missing  NA=Not Applicable  NV=Not Visible

7.3

Exterior Comments

Case Number: 093-601378

7

Snow Enterprises, LLC

At the time of the inspection, the exterior of the structure was in acceptable condition with noted

deficiencies.

Case Number: 093-601378

8

Snow Enterprises, LLC

8

Roof

This portion of the inspection covers general exterior roofing component checkpoints of the subject

property such as roof coverings (shingles, flashing, skylights, chimneys, etc.), structural elements of the

roof (trusses, rafters, ceiling foists, etc.), roof drainage systems, etc.

8.1

General Roof Information

Roof Type: Gabled

Gutter Type: Aluminum

Method to Observe Attic: None

Method to Observe Roof: Ladder

Number of Layers: 1

Attic Vent Type: Soffit, Gable

Roofing Material: Asphalt

8.2

Roof Checkpoints

Checkpoint

Rating

Comment

Shingle Cond.:

S

Flashing/Joints:

S

Soffits/Fascias:

S

Skylights:

NA

Vent Pipes:

S

Chimney:

NA

Gutters:

S

Downspouts:

MR

There are  damaged downspouts.

Attic Ventilation:

S

Attic Water:

NV

Attic Insulation:

NV

*Structural Cond.:

S

*Sheathing Cond.:

NV

Truss:

NV

Roof Exhaust Fan(s):

NA

Key:  Y=Yes  N=No  S=Satisfactory  U=Unsatisfactory  MR=Marginal  MG=Missing  NA=Not Applicable  NV=Not Visible

8.3

Roof Comments

At the time of the inspection, there were apparent deficiencies noted regarding the roof of the structure.

Case Number: 093-601378

9

Snow Enterprises, LLC

9

Plumbing

This portion of the inspection covers general plumbing checkpoints of the subject property such as interior

water supply and distribution system, interior waste drains and vent system, hot water system, fuel storage

and distribution system, and sump pump.

9.1

General Plumbing Information

Waste Disposal: Septic

Waste Piping: PVC

WH Size: 30 gallons

WH Manufacturer: Rheem

WH Model: RBa03855c13027

Water Supply: Municipal

Water Piping: Copper

9.2

Plumbing Checkpoints

Checkpoint

Rating

Comment

Bar Sinks:

NA

Bath Fixtures:

S

Connections:

MR

Interior Spa/Hot Tub:

NA

Interior Vent:

NA

Kitchen Sink:

MR

There are cut pumbing lines under the kitchen sink.

Laundry Tub:

NA

Main Shut Off:

S

Pressure Relief Valve:

S

Pressure Tank:

NA

Septic Location:

S

Septic System:

NV

Sewer Drainage:

S

Shower Pan:

NV

Sprinkler System:

NA

Storage Tanks:

NA

Vent System:

S

Water Filter:

NA

Water Heaters:

S

Water Meter:

S

Water Softener:

NA

Water Supply:

S

Well:

NA

Well Location:

NA

Well/Sump Pump:

NA

Key:  Y=Yes  N=No  S=Satisfactory  U=Unsatisfactory  MR=Marginal  MG=Missing  NA=Not Applicable  NV=Not Visible

9.3

Plumbing Comments

The plumbing system was not in working condition at the time of the inspection. The water was active at

the time of the inspection, there were two leaking shut off valves at the exterior of the structure.

Case Number: 093-601378

10

Snow Enterprises, LLC

There is an irrigation pump at the structure.

Wells and septic systems, if present, are inspected only for the presence of obvious visible defects.  The

water quality and flow capacity of wells is not determined and the full operational functionality of septic

systems cannot be determined due to the unavailability of water and the extended non-use of the system.

This report reflects general conditions noted during the time of the inspection.  Systems such as HVAC,

Plumbing, and Electrical because of their nature and complexity are subject to deterioration or breakdown

over time that cannot be predicted.

Because of this, prospective buyers are strongly urged to obtain a full home inspection prior to

purchase.

Case Number: 093-601378

11

Snow Enterprises, LLC

10

Electrical

This portion of the inspection covers general electical checkpoints of the subject property such as service

entrance conductors, service equipment, main distribution panels, voltage ratings, a representative number

of installed ceiling fans, lighting fixtures, switches and receptacles, ground fault circuit interruptors,

smoke detectors, etc.

10.1

General Electrical Information

Additional Space Available: Yes

Box Location: Garage

Capacity: 150A 120-240V

Conductor Type: Aluminum

General Wiring: Good

Num. of Disconnects: 1

Panel Manufacturer: Square D

Panel Type: Breaker

Wiring: Copper

10.2

Electrical Checkpoints

Checkpoint

Rating

Comment

Applicance Wiring:

S

Bath GFCI:

S

Breaker Cond.:

S

Exterior GFCI:

NA

Exterior Wiring:

S

Ground/Bonding:

S

HVAC Wiring:

S

Interior Wiring:

S

Kitchen GFCI:

S

Lighting Fixtures:

S

Panel Box:

S

Rec. Location:

S

Service Attach:

S

Service Meter:

S

Sub Panel Box:

S

Key:  Y=Yes  N=No  S=Satisfactory  U=Unsatisfactory  MR=Marginal  MG=Missing  NA=Not Applicable  NV=Not Visible

10.3

Electrical Comments

The electrical system was in working condition at the time of the inspection. The system was powered up

using a generator.

Electrical systems, if not active, are tested using 220 volt generators.

This report reflects general conditions noted during the time of the inspection.  Systems such as HVAC,

Plumbing, and Electrical because of their nature and complexity are subject to deterioration or breakdown

over time that cannot be predicted.

Because of this, prospective buyers are strongly urged to obtain a full home inspection prior to

purchase.

Case Number: 093-601378

12

Snow Enterprises, LLC

11

HVAC

This portion of the inspection covers general HVAC checkpoints of the subject property such as

permanently installed heating system and its controls, chimneys, heat distribution system, including fans,

pumps, and ducts, and automatic safety controls.

Normal operating control of the central air conditioning system and the distribution system, etc.

Insulation vapor barriers, ventilation of attic and foundation, kitchen, bathroom and laundry venting

systems, and the operation of any readily accessible attic ventilation fan when temperature permits, etc.

11.1

General HVAC Information

Inside Unit Brand: Not Visible

Outside Unit Brand: Goodman

Inside Model No.: Not Visible

Outside Model No.: 0406161759

Inside Unit Type: Electrical

Outside Unit Type: Electrical

11.2

HVAC Checkpoints

Checkpoint

Rating

Comment

A/C Component Cond.:

S

Boiler:

NA

Coil:

S

Coil Fins:

S

Condens. Pipe:

S

Controls:

S

Draft Device:

NA

Duct Work:

S

Electric Heat:

S

An electric forced air unit supplies the heat.

Evaporator:

NV

Fans:

S

Filter:

MR

The HVAC filter needs to be replaced.

Fireplace:

NA

Flue Pipe/Draft:

NA

Furnace System:

NA

Gas Lines:

NA

Heat Exchanger:

NA

Heat Pump:

NA

Inside Fan Motor:

S

Oil Tank:

NA

Oil Tank Vent:

NA

Refrigerant Line:

S

Supply Returns:

S

Temp. Drop Test:

NA

Thermostat:

S

Vapor Barrier:

NV

Ventilation:

S

Key:  Y=Yes  N=No  S=Satisfactory  U=Unsatisfactory  MR=Marginal  MG=Missing  NA=Not Applicable  NV=Not Visible

Case Number: 093-601378

13

Snow Enterprises, LLC

11.3

HVAC Comments

The heating system was  in working condition when the structure was connected to a 220V generator. The

AC unit was visually tested due to the low temperature. There is a window AC unit present at the

structure.

This report reflects general conditions noted during the time of the inspection.  Systems such as HVAC,

Plumbing, and Electrical because of their nature and complexity are subject to deterioration or breakdown

over time that cannot be predicted.

Because of this, prospective buyers are strongly urged to obtain a full home inspection prior to

purchase.

Case Number: 093-601378

14

Snow Enterprises, LLC

12

Interior

The interior portion of the inspection covers checkpoints involving the interior walls, ceilings, floors,

steps, cabinets, doors, and windows.

12.1

General Interior Information

There are no general information points in this section.

12.2

Interior Checkpoints

Checkpoint

Rating

Comment

Cabinets:

MR

There are damaged cabinets.

Ceilings:

S

Closets:

S

Countertops:

S

Interior Debris:

S

Detectors:

S

Door Hardware:

S

Doors:

S

Dryer Vent:

S

Floor:

MR

This structure has stained carpets.

Mold:

NV

Railings:

NA

Stairwells:

NA

Steps:

NA

Walls:

MR

There are damaged walls.

Windows:

MR

There are boarded windows from missing AC window units.

Key:  Y=Yes  N=No  S=Satisfactory  U=Unsatisfactory  MR=Marginal  MG=Missing  NA=Not Applicable  NV=Not Visible

12.3

Interior Comments

At the time of the inspection, the interior of the structure was in satisfactory condition with noted

deficiencies.

Case Number: 093-601378

15

Snow Enterprises, LLC

13

Appliances

The kitchen appliance portion of the inspection covers checkpoints involving the observation and

operation of the refrigerator, dishwasher, range, trash compactor, garbage disposal, ventilation equipment,

microwave and any other permanently installed appliances.

13.1

General Appliances Information

There are no general information points in this section.

13.2

Appliances Checkpoints

Checkpoint

Rating

Comment

Dishwasher:

MG

The dishwasher is missing.

Disposal:

NA

The garbage disposal is not applicable.

Dryer:

MG

The dryer is missing.

Microwave:

NA

Oven:

NA

Range Hood:

S

Range/Stove:

S

Refrigerator:

MG

The refrigerator is missing.

Washer:

MG

The washing machine is missing.

Other:

NA

Key:  Y=Yes  N=No  S=Satisfactory  U=Unsatisfactory  MR=Marginal  MG=Missing  NA=Not Applicable  NV=Not Visible

13.3

Appliances Comments

The appliances that were present were in acceptable condition at the time of the inspection.

Case Number: 093-601378

16

Snow Enterprises, LLC

14

HOA Information

Country club estates home owner association

15

Code Violations

There are no known code violations.

16

Pending Litigation

There is no known pending litigation.

17

Demo Orders

There are no known property demo orders.

Case Number: 093-601378

17

Snow Enterprises, LLC

18 – Radon Gas and Mold Notice

U.S. Department of Housing

and Release Agreement

and Urban Development

Office of Housing

Federal Housing Commissioner

Property Case #:

Property address:

PURCHASERS ARE HEREBY NOTIFIED AND UNDERSTAND THAT RADON GAS AND

SOME MOLDS HAVE THE POTENTIAL TO CAUSE SERIOUS HEALTH PROBLEMS.

Purchaser acknowledges and accepts that the HUD-owned property described above (the “Property”) is being offered for sale

“AS IS” with no representations as to the condition of the Property. The Secretary of the U.S. Department of Housing and

Urban Development, his/her officers, employees, agents, successors and assigns (the “Seller”) and

,

an independent management and marketing contractor (“M & M Contractor”) to the Seller, have no knowledge of radon or

mold in, on, or around the Property other than what may have already been described on the web site of the Seller or M & M

Contractor or otherwise made available to Purchaser by the Seller or M & M Contractor.

R

adon is an invisible and odorless gaseous radioactive element. Mold is a general term for visible growth of fungus, whether

it is visible directly or is visible when barriers, such as building components (for example, walls) or furnishings (for example,

carpets), are removed.

Purchaser represents and warrants that Purchaser has not relied on the accuracy or completeness of any representations that

have been made by the Seller and/or M & M Contractor as to the presence of radon or mold and that the Purchaser has not

relied on the Seller’s or M & M Contractor’s failure to provide information regarding the presence or effects of any radon or

mold found on the Property.

R

eal Estate Brokers and Agents are not generally qualified to advise purchasers on radon or mold treatment or its health and

safety risks. PURCHASERS ARE ENCOURAGED TO OBTAIN THE SERVICES OF A QUALIFIED AND

EXPERIENCED PROFESSIONAL TO CONDUCT INSPECTIONS AND TESTS REGARDING RADON AND

MOLD PRIOR TO CLOSING. Purchasers are hereby notified and agree that they are solely responsible for any required

remediation and/or resulting damages, including, but not limited to, any effects on health, due to radon or mold in, on or

around the property.

I

n consideration of the sale of the Property to the undersigned Purchaser, Purchaser does hereby release, indemnify, hold

harmless and forever discharge the Seller, as owner of the Property and separately, M & M Contractor, as the independent

contractor responsible for maintaining and marketing the Property, and its officers, employees, agents, successors and

assigns, from any and all claims, liabilities, or causes of action of any kind that the Purchaser may now have or at any time in

the future may have against the Seller and/or M & M Contractor resulting from the presence of radon or mold in, on or

around the Property.

Purchaser has been given the opportunity to review this Release Agreement with Purchaser’s attorney or other representatives

of Purchaser’s choosing, and hereby acknowledges reading and understanding this Release. Purchaser also understands that

the promises, representations and warranties made by Purchaser in this Release are a material inducement for Seller entering

into the contract to sell the Property to Purchaser.

Dated this ____ day of ____________, 20__.

Purchaser’s Signature

Purchaser’s Signature

Purchaser’s Printed Name

Purchaser’s Printed Name

Form HUD-9548-E (6/2004)

093-601378

7406 Duke Dr

Hudson, FL 34667

NHMS

Case Number: 093-601378

18

Snow Enterprises, LLC

19

Environmental Issues

There are no known property environmental issues.

Case Number: 093-601378

19

Snow Enterprises, LLC

20 – ENVIRONMENTAL COMPLIANCE RECORD

SINGLE FAMILY PROPERTY DISPOSITION

FHA Case Number:

Property Address:

COMPLIANCE FINDINGS

SOURCE / DOCUMENTATION

1. HISTORIC PRESERVATION

Property

…

is

…

is not listed on the National Register of

Historic Places.

Property

…

is

…

is not located in an Historical District.

Note:

An appropriate deed restriction will be required if

property meets either of the foregoing conditions.

2. FLOODPLAIN

Property

…

is

…

is not located within the 100-year

floodplain (Zones A and V).

Note:

Flood insurance may be required.

3

.

AIRPORT RUNWAY CLEAR ZONES (24 CFR 51D)

Property

…

is

…

is not located within boundary of runway

zone.

If “yes”,



Has the airport operator declined to acquire the

property?

…

yes

…

no



A signed disclaimer is required (24 CFR Part 51D).

4. SUMMARY

Additional actions

…

are

…

are not required on the basis of the findings above.  If additional actions are required, describe them

in an attachment.

NOTE: OTHER ENVIRONMENTAL STATUES, EXECUTIVE ORDERS AND AUTHORITIES

The remaining statutes and authorities cited at 24 CFR 50.4 do not require compliance because they are not relevant to property disposition

actions which do not involve new construction.

Preparer:

________________________________________________

Title:

Date:

Supervisor:

________________________________________________

Title:

Date:

093-601378

7406 Duke Dr, Hudson, FL 34667

Case Number: 093-601378

20

Snow Enterprises, LLC

1. Subdivison Sign

2. Front Elevation

3. Address

4. Missing Screen

5. Pk Sign

6. Address

7. Soffits

8. Damaged Eave

9. Irrigation

10. Damaged Fence

11. Side Elevation

12. Vent

Case Number: 093-601378

21

Snow Enterprises, LLC

13. Electrical Meter

14. Electrical Meter

15. Electric Company Tag

16. Main Breaker

17. Shutoff

18. Shutoff

19. Shed

20. Shed Inteiror

21. Garage

22. Garage

23. Shed Secured

24. Shed Secured

Case Number: 093-601378

22

Snow Enterprises, LLC

25. Rear Elevation

26. Rear Of Property

27. Pump

28. Hvac

29. Hvac Information

30. Side Elevation

31. Gutter And Downspout

32. Roof

33. Shutoff

34. Side Elevation

35. Damaged Eave

36. Interior Room

Case Number: 093-601378

23

Snow Enterprises, LLC

37. Damaged Floor

38. Thermostat

39. Interior Room

40. Detector

41. Bathroom

42. Plumbing

43. Shower Head

44. Interior Room

45. Damaged Wall

46. Kitchen

47. Kitchen

48. Rangehood

Case Number: 093-601378

24

Snow Enterprises, LLC

49. Rangehood

50. Sink

51. Plumbing

52. Missing Refrigerator

53. Inteiror Room

54. Inteiror Room

55. Inteiror Room

56. Window Unit Covered

57. Marble Window Sill

58. Missing Washer And Dryer

59. Inteiror Room

60. Interior Room

Case Number: 093-601378

25

Snow Enterprises, LLC

61. Window Ac

62. Damaged Floor

63. Damaged Floor

64. Damaged Floor

65. Water Heater

66. Bathroom

67. Shower Pan

68. Shower Head

69. Attic

70. Irrigation Pump

71. Garage Door Opener

72. Electric Panel

Case Number: 093-601378

26

Snow Enterprises, LLC

73. Electric Main

74. Electrical Information

75. Electrical Panel

76. Water Heater Information

77. Rear Door

78. Bthroom

79. Damaged Floor

80. Thermostat

81. Damged Wall

82. Water Heater Control

83. Relief Valve

84. Active Water

Case Number: 093-601378

27

Snow Enterprises, LLC

85. Shut Off Leak

86. Shut Off Leak

87. Water Meter

88. Water Meter Serial Number

89. Irrigation Vlave

90. Roof

91. Roof

92. Illumination

93. Illumination

94. Illuminaton

95. Attic

96. Hookup

Case Number: 093-601378

28

Snow Enterprises, LLC

97. Hookup

98. Damaged Cabinet

99. Roof

100. Garage Secured

101. Sign In Sheet

102. Damaged Door

103. Missing Hardware

104. Missing Hardware

105. Damaged Shutter

106. Septic Service